## Slide 1
SUMMA · SUBSYSTEM 3
MOFN HS OLS Configurator
Status recap & engine + catalog roadmap
Nokia 1830 GX OLS · BoM generator for hyperscaler MOFN deployments
Quang — Nokia Optical Networks, Sales Engineering (Vietnam)
Prepared 25 Jun 2026 · Engine v3.1 · Catalog HS Configurator v3.1.xlsx

## Slide 2
WHAT IT IS
A capability-rule BoM engine for MOFN OLS builds
The configurator (mofn.html) turns a handful of deployment inputs into a real, shippable Bill of Materials for Nokia 1830 GX optical line systems at hyperscaler Managed Optical Fiber Network sites — chassis, cards, power and rack space, with the reasoning shown for every pick.
Inputs
Band · fiber pairs (1–8) · distance + span · amp strategy · ROADM/MUX term · rack & power budget · release ceiling
Engine
Band-hierarchy selection, distance-driven topology, BIDI/uni-dir qty math, slot-based chassis consolidation, family enforcement
Output
Per-node + per-ILA BoM, power roll-up (typ/max@40/max@55), rack-budget check, gap banners, full reasoning panel
Why it exists: an SE can size a full OLS link — e.g. 1800 km — into a quotable BoM in minutes, instead of hand-building it against the PowerDraw spreadsheet and the part catalog.
Summa · MOFN HS OLS Configurator
2

## Slide 3
DONE · ENGINE
Four engine generations shipped
v1
xlsx-direct
18 fixed scenario codes lifted straight from the catalog spreadsheet. 63 parts. Identified empty/partial scenarios + systemic OMD gaps.
v2
capability rules
Band hierarchy (C++ covers C, L++ covers L). FP slider 1–8. ILA strategy split (Raman / EDFA / P2P). P2P ROADM-vs-MUX toggle. L-only band added.
v3
distance-driven
Topology from km: spans = ⌈total/span⌉, term = 2 endpoints, ILA = spans−1. Per-PN BIDI vs uni-directional qty math. Universal ROADM/MUX term.
v3.1
current
Super C+L X+L ROADM combo, hybrid→EDFA+Raman fallback, mixed-ILA split, RPBL exclusion, OTDR toggle, slot-based chassis + family enforcement.
Refactor path: a brittle scenario lookup became a rule engine that produces real distance- and direction-aware BoMs.
Summa · MOFN HS OLS Configurator
3

## Slide 4
DONE · DELIVERED ASSETS
Catalog, dashboard and power data — all live
55
part numbers
single source of truth in HS Configurator v3.1.xlsx — 55 PNs × 21 columns, regenerates the engine's PARTS array.
11
portfolio sections
dashboard.html renders the full Nokia hyperscaler portfolio — term chassis, OMD, OCC, ROADM, amps, ILA EDFA/Raman/Hybrid.
0%
PowerDraw delta
PowerDraw R9.0 integrated; per-row typ/max@40/max@55 power matches PowerDraw to 0% on the 1800 km / 60 km baseline.
Also shipped
Hyperscaler news + APAC datacenter map on the dashboard
Reasoning panel — every engine rule explained per BoM
Gap banners (hybrid fallback, Super C+L combo, etc.)
Rack & power budget check (PEM-input headroom)
STRICT / RELAX release-ceiling gating with roadmap flags
Repo-ready as v1 — engine logic archived in markdown
Summa · MOFN HS OLS Configurator
4

## Slide 5
DONE · ENGINE INTELLIGENCE
The non-obvious rules the engine already enforces
Band hierarchy
Wider-band HW serves narrower deployments — Y covers all, X/W cover Super C, Z covers C+L. Tiebreaker prefers the closest fit, not the widest card.
Distance topology
1800 km ÷ 60 km span → 2 term nodes + 29 ILA sites, computed automatically. Qty scales with site count, not a fixed scenario.
BIDI vs uni-dir
ILA EDFA / IRB cards are bidirectional (×1 per FP); RPB Raman cards are uni-directional (×2 per FP per site). Modeled per-PN via a bidi flag.
Slot-based chassis
ROADM/D-prefix/4-fiber = 2 slots; rest = 1. Engine picks the smallest chassis that fits and consolidates (1× G34L over 2× G32E).
Family enforcement
G3S-G/H/R cards → full chassis (G31/G32/G34L); C/D cards → compact (G34c/G32c/G38c). Never mixes families at one site.
Smart fallbacks
Hybrid not GA → EDFA+Raman; no Y-suffix ROADM → RD32-X + RD32-L combo; ROADM's integrated EDFA → drops the separate term PBA.
Summa · MOFN HS OLS Configurator
5

## Slide 6
CURRENT BLOCKERS · CATALOG & PLM
What the engine cannot fully build today
No Super C+L OMD (Y-suffix)
HIGHEST PRIORITY
Super C+L MUX-based termination has no part in the catalog.
No Super C+L EDFA-only ILA
HIGH
Super C+L with an EDFA-only ILA strategy returns no part — only Raman/hybrid Y cards exist.
FP4 Super C+L is roadmap-only
HIGH
Only buildable with R10.1 hardware: G2RPB4M-Y2 + H4IRB4SG-Z2. Zero GA path today.
No native FP5–8 cards
MEDIUM
FP5–7 must use 2× FP4 multi-fiber sets (under-utilised); FP8 = 2× FP4 exactly.
G34L (L-band 700 mm) not GA
MEDIUM
R9.2 tbc — blocks L-only deployments at the term node.
L-band ROADM thin
MEDIUM
Only RD32TH-L0 (R10.0); no L-band 66-deg ROADM for high-degree L nodes.
Red = no GA path at all · Amber = roadmap-gated or works but inefficient. All six are catalog/PLM-driven, not engine bugs.
Summa · MOFN HS OLS Configurator
6

## Slide 7
ROADMAP · NEXT 2–3 VERSIONS
Where the engine and catalog go next
v3.2
NEAR-TERM ENGINE
Channel-count filter so OMD pick is SE-driven, not first-match
Term ROADM degree filter (9 / 20 / 32 / 66-deg)
Protection scheme (1+1 / OMSP / OCh-P) → extra cards & diversity
Catalog sync as R9.2 / R10.0 parts GA
v4
NEXT MAJOR ENGINE
Encryption variant modeling (D encrypted vs N clear)
Multi-degree node topology (today term = 1-degree end of chain)
AC/DC power-feed → PSU SKU selection
Retire/confirm 11 never-assigned catalog parts
Catalog
PLM-DRIVEN, RFS-TIED
Add Y-suffix OMD → closes Super C+L MUX gap
Add Y-suffix EDFA-only ILA
FP4 Super C+L GA via R10.1 (G2RPB4M-Y2, H4IRB4SG-Z2)
G34L GA @ R9.2 + RD32TH-L0 @ R10.0 → unlock L-only
Priority order: close the Super C+L MUX/EDFA gaps and degree/channel filters first — they unblock the most real quotes.
Summa · MOFN HS OLS Configurator
7

## Slide 8
OPEN ACTIONS · PLM
Questions to close with the product line
1
What is the firm R10.1 RFS date — and is there any interim path for FP4 Super C+L before then?
2
Is a Y-suffix OMD (GQS-OMD-Y*) planned, or must Super C+L always terminate on a ROADM?
3
Will D2ILASGM get a Y-suffix EDFA-only variant for Super C+L EDFA strategy?
4
Confirm L-band RFS dates (G34L R9.2, RD32TH-L0 R10.0) — and is L-only a sales priority?
5
Should OMD selection be channel-count driven (32/40/42/48/64) rather than first-match?
6
Should the SE be able to filter the term ROADM by degree (9/20/32/66) for node connectivity?
7
The 11 never-assigned catalog parts — intended use, or mark for retirement?
Blue = blocks a GA build path today. Gray = engine-UX refinement.
Summa · MOFN HS OLS Configurator
8

## Slide 9
WHERE WE STAND
v3.1 is a real BoM tool — now close the catalog gaps
Shipped — 4 engine generations, 55-PN catalog, populated dashboard, PowerDraw at 0% delta.
Next engine — v3.2 — channel-count + ROADM-degree + protection filters, then v4 encryption & multi-degree.
Next catalog — Y-suffix OMD & EDFA ILA, FP4 Super C+L at R10.1, L-band at R9.2 / R10.0.
Summa · MOFN HS OLS Configurator · Nokia ON Sales Engineering, Vietnam · GMT+7